## Slide 1
Channel Assignment Methods

## Slide 2
Channel Assignment Strategy
Min-interference and Connectivity-Oriented Partially Overlapped Channel Assignment (MC-POCA)
Utilize partially overlapped channels instead of 3 non-overlapped channels
P. Kyasanur and N.H. Vaidya, Routing and Link-layer Protocols for Multi-Channel Multi-Interface Ad Hoc Wireless Networks, SIGMOBILE Mobile Computing and Communications Review, vol. 10, no. 1, pp.
Partially Overlapped Assignment
Start
Calculate links assignment rank
Generate decreasing links queue
End
Partially Overlapped Channel Assignment
Select channel by score function
Routing Selection

## Slide 3
Strategy Advantages
Low time complexity
Effectively utilized partially overlapped channels
Easy to assess the link interference

## Slide 4
Strategy Drawbacks
Score function 1
Count how many the link pairs which have interference for each channel
Select the best channel with the minimum interference link pairs to assign
Example of a conflict graph
Figure Scource: https://www.researchgate.net/figure/The-conflict-graph-for-the-five-node-network_fig2_51915978

## Slide 5
Strategy Drawbacks
Score function 2
Get the distance of closest nodes of 2 links
Get ir(p,l), the interference distance ratio
For any assigned links, sum interference up and then choose the best channel

## Slide 6
Strategy Drawbacks
Partially overlapped channel network may have much more interference link pairs
Node Interference range may not reasonable for calculating link interference range
Current assigned channel will interference unassigned empty links

## Slide 7
Strategy Drawbacks
Algorithm Structure
Once a link is assigned with certain channel, it’s impossible to modify or revise
The rank of links may change during the algorithm, but priority queue never update
Sequential Forward Channel Assignment
Figure Scource: https://www.cc.gatech.edu/~bboots3/CS4641-Fall2018/Lecture16/16_FeatureSelection.pdf

## Slide 8
Score Function J(w) Design
Step 1. Measure interferenced by other links
Step 2. Measure interference assigned links
Step 3. Measure interference unassigned empty links

## Slide 9
Score Function J(w) Design
Step 1. Measure interferenced by other links

## Slide 10
Score Function J(w) Design
Constraints
Define the receiver SNR as a threshold.
is predefined because wireless mesh network utilizes OQPSK or 64QAM demodulation

## Slide 11
Score Function J(w) Design
Score for Step 1
Define the function
One example of function
A(0) means all assigned links which interference range could cover link

## Slide 12
Score Function J(w) Design
Step 2. Measure interference assigned links

## Slide 13
Constraints 1
Score Function J(w) Design
For each assigned link, we can define a SNR threshold.

## Slide 14
Constraints 2
Score Function J(w) Design
Calculate total variance of assigned links

## Slide 15
Score Function J(w) Design
Score for Step 2
One example of function
B(0) means all assigned links within the interference range of link

## Slide 16
Score Function J(w) Design
Step 3. Measure interference unassigned empty links

## Slide 17
Score Function J(w) Design
Score for Step 3
is the smallest index the node appears as a receiver in the link priority queue

## Slide 18
Score Function J(w) Design
Score for Step 3
One example of function
is a discrete function which means that if assigning channel at the edge of frequency bandwidth, there will be more available partially overlapped channels for other links

## Slide 19
Score Function J(w) Design
One example of wireless mesh network

## Slide 20
Score Function J(w) Design
Wavelength Estimation
Figure Scource: https://en.wikipedia.org/wiki/List_of_WLAN_channels
Estimate as 0.12m to simplify calculation

## Slide 21
Sequential Forward Channel Assignment (SFS)
Algorithm Structure Design
Solution Space for SFS

## Slide 22
Algorithm Structure Design

## Slide 23
Drawbacks
Algorithm Structure Design
Once a link is assigned with certain channel, it’s impossible to modify or revise
The rank of links may change during the algorithm, but priority queue never update
One example of wireless mesh network

## Slide 24
Sequential Floating Forward Channel Assignment (SFFS)
Algorithm Structure Design
Solution Space for SFFS
Future work